## Slide 1: CS 485 Autonomous Robotics Localization I
Prof. Xuesu Xiao
George Mason University
Slides Credits: Gregory Stein

## Slide 2: Logistics Notes
Good job on The BARN Challenge!
Start your open-ended project soon!
  Three weeks till mid-project presentation…
  Five weeks till final project presentation…
Homework 3 is due next week on November 2 before class.

## Slide 3: Reminder…
The Kalman Filter: continuous (gaussian) filtering

## Slide 4: Last week, just about everything was Gaussian: Motion Model
How do we compute the “uncertainty” on each?

## Slide 5: Last week, just about everything was Gaussian: Sensor Model
How do we compute the “uncertainty” on each?
How do we incorporate the GPS observations?

## Slide 6: However, our graphical representation was more general
The graphical representation will look pretty much the same:

## Slide 7: The EKF is necessary when we have a robot with orientation
If we have uncertainty in yaw, the motion model becomes nonlinear:
From: https://cs.gmu.edu/%7Ekosecka/cs685/cs685-11-sensor-motion-models.pdf

## Slide 8: The EKF is necessary when we have a robot with orientation
If we have uncertainty in yaw, the motion model becomes nonlinear:
From: https://cs.gmu.edu/%7Ekosecka/cs685/cs685-11-sensor-motion-models.pdf

## Slide 9: Will the EKF help us with the “Doors” example from earlier?

## Slide 10: Will the EKF help us with the “Doors” example from earlier?
Hmm, probably not. We approximate the distribution as being Gaussian, so we’d lose the multi-peaked structure.
We’ll talk more about how to handle more complex probability distributions like these.

## Slide 11: Motion and Sensor Models

## Slide 12: Robot motion is inherently uncertain
Last week, we talked about both Gaussian Motion and Observations, but in general, neither will be. We need ways to represent non-Gaussian models.

## Slide 13: Reminder: graphical representations of joint probability distributions

## Slide 14: Consider a differential drive robot: Wheel encoders tell us the rotation

## Slide 15: Dead Reckoning: integrating motion measurements to compute position
Mathematical procedure for determining the present location of a vehicle.
Achieved by calculating the current pose of the vehicle based on its velocities and the time elapsed.
Last week, we talked about this in the context of Gaussian Motion and the noisy motion estimates:

## Slide 16: Even if we could perfectly integrate the wheel encoders, our measurements are noisy
Sources of motion error:

## Slide 17: Odometry Model

## Slide 18: A noise model for odometry for a differential drive robot

## Slide 19: A noise model for odometry for a differential drive robot

## Slide 20: Calculating the posterior from our (noisy) motion model:
P(x’ | x, u)

## Slide 21: We repeatedly apply this motion model to get the posterior on the position

## Slide 22: How do we use this motion model?
A Kalman Filter requires that everything be Gaussian.
The Extended Kalman Filter approximates the nonlinear system as being Gaussian, which works fairly well for a while, but over time—especially when dead reckoning, and there are no updates from other measurements—you start to lose accuracy.
What if we tried sampling again?

## Slide 23: Reminder: Let’s say you wanted to compute the area of a circle…
What if you printed out the shape and threw a dart at it?
If you aim is totally random, what’s the probability you’re inside the square, but not the circle?
Image Credit
P = 1 - Acircle / Asquare

## Slide 24: Reminder: Monte Carlo Sampling
Idea: we throw a lot of darts and the number that are inside the circle will tell us what it’s area is.
As we get more samples, our approximation gets better.
In many cases, this can be way faster than trying to get an exact solution.
Image: Wikipedia

## Slide 25: Now, we have a probability distribution that we cannot easily write down…
We can sample values from the distribution and we’ll represent that distribution with points drawn from that distribution.
Idea: we have some random value x ~ P(X). If we can draw many values of x, we can use those as a stand in for the distribution. With enough samples, we can compute any value we would want that requires the distribution:

## Slide 26: Sample-based Density Representation

## Slide 27: Sampled Normal Distribution

## Slide 28: Sampled Triangular Distribution

## Slide 29: We can use this to sample from our noisy motion model

## Slide 30: We can use this to sample from our noisy motion model

## Slide 31: We can use this to sample from our noisy motion model

## Slide 32: Overview: Non-Gaussian Motion Models

## Slide 33: Sensor Models
How do we measure the world around us?

## Slide 34: There are many ways robots sense the world

## Slide 35: LiDAR: Light Detection and Ranging
Video from the MIT Team

## Slide 36: Velodyne makes great LiDARs
The Puck
Link: https://velodynelidar.com/products/puck/

## Slide 37: Proximity Sensors: lasers and sonars

## Slide 38: Beam-based (probabilistic) sensor model

## Slide 39: Beam-based (probabilistic) sensor model

## Slide 40: Typical types of errors for beam-like measurements

## Slide 41: Proximity measurements and sources of noise and error

## Slide 42: Beam-based proximity model

## Slide 43: Beam-based proximity model

## Slide 44: Beam-based proximity model

## Slide 45: We can collect data for ranges of an object a known distance away

## Slide 46: We can determine the model parameters by fitting to the data

## Slide 47: Here are how the model compares to the data:

## Slide 48: Here are some examples of laser scans in a physical environment

## Slide 49: Summary of a beam-based sensor measurement model

## Slide 50: What about a “scan-based” measurement model?

## Slide 51: What about a “scan-based” measurement model?

## Slide 52: What about a “scan-based” measurement model?

## Slide 53: What about a “scan-based” measurement model?

## Slide 54: What about a “scan-based” measurement model?

## Slide 55: We can use probabilistic sensor models to perform multiple operations we may need:

## Slide 56: Will the EKF help us with the “Doors” example from earlier?

## Slide 57: Will the EKF help us with the “Doors” example from earlier?
Hmm, probably not. We approximate the distribution as being Gaussian, so we’d lose the multi-peaked structure.
Now, we’ll talk more about how to handle more complex probability distributions like these.

## Slide 58: What if we discretize the space?
The Belief can be split into ”buckets” each with some “weight”
Motion “moves” the probability mass around
Measurements update the belief.
[Same as before, but no longer continuous.]

## Slide 59: What if we discretize the space?
The Belief can be split into ”buckets” each with some “weight”
Motion “moves” the probability mass around
Measurements update the belief.
[Same as before, but no longer continuous.]

## Slide 60: The Discrete Bayes Filter Implementation

## Slide 61: Example application: grid-based localization Figure out where we are from scans

## Slide 62: Sample-based localization
We get sensor observations and we know how much we move between observations

## Slide 63: By getting sensor measurements and connecting them with motion, we can figure out the pose:

## Slide 64: Introducing the “Particle Filter”

## Slide 65: Particle filter: mathematical formalism

## Slide 66: Function approximation using particles

## Slide 67: Rejection Sampling

## Slide 68: We don’t often want to sample everywhere, so we can use “Importance Sampling”

## Slide 69: Particle Filtering Start with a uniform distribution of particles

## Slide 70: Particle Filtering We next compute weights from an observation

## Slide 71: Particle Filtering We move/update particles using the motion model and resample

## Slide 72: Particle Filtering We next compute weights from an observation

## Slide 73: Particle Filtering We move/update particles using the motion model and resample

## Slide 74: Particle Filter Algorithm

## Slide 75: Particle Filter Algorithm

## Slide 76: Particle Filter Algorithm

## Slide 77: How does resampling work?

## Slide 78: Mobile Robot Localization

## Slide 79: Mobile Robot Localization
Non-Gaussian Motion Model
Very non-Gaussian sensor model

## Slide 80: Particle Filtering Example Start with a uniform particle distribution

## Slide 81: Particle Filtering Example Get an observation

## Slide 82: Particle Filtering Example Move and resample

## Slide 83: Particle Filtering Example Get an observation

## Slide 84: Particle Filtering Example Move and resample

## Slide 85: Particle Filtering Example Get an observation

## Slide 86: Particle Filtering Example Move and resample

## Slide 87: We can do the same thing but with vision Vision-based localization

## Slide 88: Vision-based localization Observation: Under a light

## Slide 89: Vision-based localization Observation: Next to a light

## Slide 90: Vision-based localization Observation: not near a light

## Slide 91: Vision-based localization Combined we can figure out where we are

## Slide 92: Limitations of particle filtering

## Slide 93: Approaches to deal with limitations

## Slide 94: Particle Filters

## Slide 95: Particle Filter Localization