## Slide 1: CS 485 Autonomous Robotics Introduction to Probabilistic Robotics I
Prof. Xuesu Xiao
George Mason University
Slides Credits: Gregory Stein

## Slide 2: Logistics
No class next Tuesday (October 3 2023).
Midterm next Thursday (October 5 2023).
The standardized BARN Challenge is due in two weeks.
Open-ended project proposal presentation in two weeks.
  5-10 min per team
  Please cover the following information:
    What problem are you trying to solve?
    Why it is worth solving?
    What are the possible approaches?
    What approach are you taking and why it is appropriate?
    What is your deliverables?
    What is your timeline?

## Slide 3: Motivation: our robot is still quite limited…
Disaster City® Texas A&M
What would you like a robot to do to help?

## Slide 4: Motivation: our robot is still quite limited…
We will learn about the fundamentals:
The core mathematical tools used to represent robots and the world
How robots move and interact
How robots sense the world
How robots understand the world
How robots …
We know how to do some of those things, but not others.

## Slide 5: Idea: Robots should augment or replace human capacity
…but humans are generally quite capable.
We can navigate spaces, even those we’ve never been before.
Humans can pick up objects and manipulate them.
We take in rich sensor information and use this to figure out where we are, the state of the world, and how we might interact with it.

## Slide 6: Capability: Motion Planning
Source: Direct Path Superfacets (Prof. Plaku)

## Slide 7: Capability: Motion Planning
Image: Wired

## Slide 8: Capability: Control
Source: Boston Dynamics

## Slide 9: Capability: Mapping
Google Cartographer for Laser-based mapping

## Slide 10: Motivation: a robot may not even know where it is in the world!
Localization will be one of the core capabilities we discuss today (and next week). The robot must use its noisy and imperfect sensors to figure out where it is in the world.
Only then can it know how to act.
We’ll start by discussing how we think about the robot’s ability to sense its surroundings and what to do when those observations are noisy and imperfect.

## Slide 11: Motivation: a robot wandering the halls
Consider a robot in a hallway.
Example from the Probabilistic Robotics textbook

## Slide 12: Motivation: a robot wandering the halls
Consider a robot in a hallway. It’s ”lost” and so its initial belief (the probability distribution over its position) is uniform:
Example from the Probabilistic Robotics textbook

## Slide 13: Motivation: a robot wandering the halls
Consider a robot in a hallway. It’s ”lost” and so its initial belief (the probability distribution over its position) is uniform:
Then the robot looks and sees this behind it:
Where’s the robot?
Example from the Probabilistic Robotics textbook

## Slide 14: Motivation: a robot wandering the halls
Consider a robot in a hallway. It’s ”lost” and so its initial belief (the probability distribution over its position) is uniform
When I receive an observation, I can update my belief
I don’t know which door, but I’m by one of them.
Example from the Probabilistic Robotics textbook

## Slide 15: Motivation: a robot wandering the halls
Next the robot moves to the right a couple meters
We know the robot has moved to the right a bit, though not quite how much, since it’s motion is a bit noisy.
Example from the Probabilistic Robotics textbook

## Slide 16: Motivation: a robot wandering the halls
Next the robot moves to the right a couple meters. It looks again… and finds another door!
The new observation is similar to the first: we know we are near a door.
Example from the Probabilistic Robotics textbook

## Slide 17: Motivation: a robot wandering the halls
Next the robot moves to the right a couple meters. It looks again… and finds another door!
The new observation is similar to the first: we know we are near a door. Yet we can combine it with our belief of where we are to refine it.
Example from the Probabilistic Robotics textbook

## Slide 18: Outline for today
Filtering Overview
Discrete Filtering (Hidden Markov Model)
Our states are discrete
Kalman Filtering
States are continuous

## Slide 19: Reading & Slide Credits
Slide Credits (from which many of the reference images have been taken or adapted):
CMU 16.385 (Temporal State Models Lecture)
GTSAM Tutorial
The Probabilistic Robotics Textbook
(Lots of other small things; referenced when appropriate.)

## Slide 20: There are many different ways to represent the state of the world “X”

## Slide 21: Let’s consider another simple example: A robot with noisy wheels wandering around
That makes sense: the robot moves but is somewhat jittery.
We go in the direction we want.

## Slide 22: Let’s consider another simple example: A robot with noisy wheels wandering around
That makes sense: the robot moves but is somewhat jittery.
We go in the direction we want.
Here’s the issue: our measurement of the wheel motion is also noisy.
The curves don’t match:
We don’t know where we are!

## Slide 23: What do we know so far?
Ideas?

## Slide 24: What do we know so far?
Ideas? What are the observations we have been given?

## Slide 25: What do we know so far?
Ideas? What are the observations we have been given?
We have the motion in x and y.
We also have a model for how to use that motion to get position: we just sum them up over time.
What else? Do I roughly know where I am? Do I have a pretty good idea where I am not?

## Slide 26: What do we know so far?
Ideas? What are the observations we have been given?
We have the motion in x and y.
We also have a model for how to use that motion to get position: we just sum them up over time.
Also, we have a “noise model”: because we can directly see the relationship between the “true” measurements and the “noisy” ones; we’re not clueless about where we are:
E.g., We know we’re not *at* x=50 by the end, but we’re not likely near the origin at x=0.

## Slide 27: We can associate “confidence bounds” on our measurements
What do we notice about the 95% bounds shown here as gray circles?
We’ll discuss where these come from later.
Key: they get bigger as we move! Why?
Each time we move, we introduce more noise.
Can we improve?
Not really… Not unless we are given more information.
Any Ideas?

## Slide 28: What if we were given some GPS measurements? Will this help?
Why might GPS help us?
A: Those measurements are based on the true position, not the noisy one.
This gives us an independent measurements of the true position, which we can use to improve our state estimate.

## Slide 29: The “GPS” here is a bit noisy, but maybe it can help us get “back on track”
Why might GPS help us?
A: Those measurements are based on the true position, not the noisy one.
This gives us an independent measurements of the true position, which we can use to improve our state estimate.
Let’s see what happens!

## Slide 30: We can combine the GPS measurements with the motion model to get the states

## Slide 31: We can combine the GPS measurements with the motion model to get the states
Before:
It’s not perfect but is certainly better.
Also, the “confidence” is better

## Slide 32: How do we do this?
That’s what we’ll work out for the rest of today

## Slide 33: First, we’ll build up our mathematical tools

## Slide 34: Crash Course: A Brief Review of Probability and notation for probability
What’s this?
The probability of getting the value b from some process.
What’s this?
The probability of getting both a and b.
What’s this?
Imagine these values are “heads” or “tails” of a coin, or some other random process.

## Slide 35: Crash Course: A Brief Review of Probability and notation for probability
What’s this?
The probability of getting the value b from some process.
What’s this?
The probability of getting both a and b.
What’s this?
Imagine these values are “heads” or “tails” of a coin, or some other random process.
Remember:

## Slide 36: Crash Course: A Brief Review of Probability and notation for probability
What’s this?
The probability of getting the value b from some process.
What’s this?
The probability of getting both a and b.
What’s this?
Imagine these values are “heads” or “tails” of a coin, or some other random process.
Remember:

## Slide 37: Crash Course: A Brief Review of Probability and notation for probability
Conditional Probability: the likelihood of getting some value b conditioned on the fact that I already know the value of a.
So what’s this?
“probability of b given a”

## Slide 38: Crash Course: A Brief Review of Probability and notation for probability
Conditional Probability: the likelihood of getting some value b conditioned on the fact that I already know the value of a.
So what’s this?
“probability of b given a”

## Slide 39: Crash Course: A Brief Review of Probability and notation for probability
Rules of conditional probability:

## Slide 40: Crash Course: A Brief Review of Probability and notation for probability
Rules of conditional probability:
From here, we can derive Bayes’ Theorem:

## Slide 41: Crash Course: A Brief Review of Probability and notation for probability
The “expectation” is a weighted sum of a function taken over some probability distribution. Let’s say we have some function “f” that takes a single argument b. We also have a probability distribution over b: P(b). The expected value of f is written as:

## Slide 42: What is the problem we are trying to solve?
We want to find the (current) state of the world based on everything we know and have observed so far.

## Slide 43: What is the problem we are trying to solve?
We want to find the (current) state of the world based on everything we know and have observed so far.
The state changes over time:
We use a sequence of random variables:
Together, a joint probability is needed to represent them all:

## Slide 44: What is the problem we are trying to solve?
We want to find the (current) state of the world based on everything we know and have observed so far.
For today: we just want to know where the robot is…
How big is this distribution?

## Slide 45: What is the problem we are trying to solve?
We want to find the (current) state of the world based on everything we know and have observed so far.
For today: we just want to know where the robot is…
How big is this distribution? Pretty big…

## Slide 46: Earlier, we saw that we could also include observations in our estimate
The total joint probability looks like this:
States are the things we want.
Observations (evidence) is what we have measured that can give use information about the states.
States
Observations (“Evidence”)

## Slide 47: Earlier, we saw that we could also include observations in our estimate
The total joint probability looks like this:
States are the things we want.
Observations (evidence) is what we have measured that can give use information about the states.
The distribution is massive.
We need a way to simplify it.
States
Observations (“Evidence”)

## Slide 48: We will make some simplifying assumptions

## Slide 49: We will make some simplifying assumptions #1: Markov Assumption
A system satisfying the Markov Property is memoryless. (okay, well what does that mean?)

## Slide 50: We will make some simplifying assumptions #1: Markov Assumption
A system satisfying the Markov Property is memoryless. (okay, well what does that mean?)
In general, the state could depend on all my history up until now:

## Slide 51: We will make some simplifying assumptions #1: Markov Assumption
A system satisfying the Markov Property is memoryless. (okay, well what does that mean?)
In general, the state could depend on all my history up until now:
If the system is Markov, there is no additional information to be gained from those earlier states and actions:

## Slide 52: What sort of system is not Markov
What about a “Fibonacci-like” system?
To figure out the next “state”, I need to add the value of the two previous states. If my “state” is only the most recent number, computing what state I’ll end up in requires using both previous states.
Can we make this system Markov?
Yes! Just have the “state” include both previous numbers.
“Every system is Markov”. All you need is a bigger/better/more complete state representation.

## Slide 53: What sort of system is not Markov
What about a “Fibonacci-like” system?
To figure out the next “state”, I need to add the value of the two previous states. If my “state” is only the most recent number, computing what state I’ll end up in requires using both previous states.
Can we make this system Markov?
Yes! Just have the “state” include both previous numbers.
“Every system is Markov”. All you need is a bigger/better/more complete state representation.

## Slide 54: What sort of system is not Markov
What about a “Fibonacci-like” system?
To figure out the next “state”, I need to add the value of the two previous states. If my “state” is only the most recent number, computing what state I’ll end up in requires using both previous states.
Can we make this system Markov?
Yes! Just have the “state” include both previous numbers.
“Every system is Markov”. All you need is a bigger/better/more complete state representation.

## Slide 55: What sort of system is not Markov
What about a “Fibonacci-like” system?
To figure out the next “state”, I need to add the value of the two previous states. If my “state” is only the most recent number, computing what state I’ll end up in requires using both previous states.
Can we make this system Markov?
Yes! Just have the “state” include both previous numbers.
“Every system is Markov”. All you need is a bigger/better/more complete state representation.

## Slide 56: We will make some simplifying assumptions #1: Markov Assumption
A system satisfying the Markov Property is memoryless.
This will also help us reduce the observation model.
The likelihood of an observation could depend on all states up until now. We’ll instead assume that an observation at a particular time, depends only on the current state:
Example: think of GPS. It doesn’t matter where I used to be. Only where I am now.

## Slide 57: We will make some simplifying assumptions #1: Markov Assumption
A system satisfying the Markov Property is memoryless.
Combined these assumptions imply that we only need the following to relate states to other states and to observations:
State Transition Model
A.k.a. a Motion Model
Observation Model

## Slide 58: We will make some simplifying assumptions #2: Stationary Process Assumption
A process is “stationary” if it does not change over time.
This means that the relationship between the state and each observation does not change over time.
In principle, the state transition and observation models could change over time, but we assume they don’t.

## Slide 59: We will make some simplifying assumptions #3: Prior State Assumption
We’ll assume that we have at least some idea of where we started.
This means that we’ll have a prior state distribution in advance:

## Slide 60: Combined, our assumptions let us rewrite the joint probability distribution
Each term is something we understand, and each is much lower-dimensional than the original.
So how do we solve it?

## Slide 61: Combined, our assumptions let us rewrite the joint probability distribution
Each term is something we understand, and each is much lower-dimensional than the original.
So how do we solve it?
Prior
Motion/State Transition Model
Observation Model

## Slide 62: It is common to represent probability distributions like these as a graph
Prior
Motion/State Transition Model
Observation Model
Nodes are random variables or input information
Edges are terms in the probability distribution
We will revisit this later!
The prior

## Slide 63: It is common to represent probability distributions like these as a graph
Nodes are random variables or input information
Edges are terms in the probability distribution
We will revisit this later!
Prior
Motion/State Transition Model
Observation Model
The prior
Including robot motion

## Slide 64: It is common to represent probability distributions like these as a graph
Nodes are random variables or input information
Edges are terms in the probability distribution
We will revisit this later!
Prior
Motion/State Transition Model
Observation Model
The prior
Including robot motion
Including observations

## Slide 65: It is common to represent probability distributions like these as a graph
Nodes are random variables or input information
Edges are terms in the probability distribution
We will revisit this later!
Prior
Motion/State Transition Model
Observation Model
The prior
Including robot motion
Including observations

## Slide 66: Discrete Filtering and the Hidden Markov Model
With a number of visuals and equations drawn from CMU 16.385 (Temporal State Models Lecture)

## Slide 67: This is an insane example… but is too good to pass up

## Slide 68: This is an insane example… but is too good to pass up
Through a hole, you can sort of make out what lane you are in

## Slide 69: This is an insane example… but is too good to pass up
We want to figure out where the car is likely to be, so we need to revisit our equation from earlier and the terms to define it:

## Slide 70: Sleepy Driver HMM Defining the terms we need
Prior
Motion/State Transition Model
Observation Model
What do these tell us?

## Slide 71: Sleepy Driver HMM Defining the terms we need
Prior
Motion/State Transition Model
Observation Model
What do these tell us? The prior?

## Slide 72: Sleepy Driver HMM Defining the terms we need
Prior
Motion/State Transition Model
Observation Model
What do these tell us? The prior?
We don’t have any info about what lane we start in.

## Slide 73: Sleepy Driver HMM Defining the terms we need
Prior
Motion/State Transition Model
Observation Model
What do these tell us? The motion model?

## Slide 74: Sleepy Driver HMM Defining the terms we need
Prior
Motion/State Transition Model
Observation Model
What do these tell us? The motion model?
We usually stay in the same lane, but switch 30% of the time.

## Slide 75: Sleepy Driver HMM Defining the terms we need
Prior
Motion/State Transition Model
Observation Model
What do these tell us? The observation model?

## Slide 76: Sleepy Driver HMM Defining the terms we need
Prior
Motion/State Transition Model
Observation Model
What do these tell us? The observation model?
We are pretty good at telling what lane we are in. Slightly more accurate in the left lane.

## Slide 77: Sleepy Driver HMM Defining the terms we need
Prior
Motion/State Transition Model
Observation Model
Also, these are probability distributions, so something must sum to 1. What is it?

## Slide 78: Temporal Inference has multiple tasks we could want to solve

## Slide 79: Temporal Inference has multiple tasks we could want to solve

## Slide 80: Let’s start with filtering Where is the robot now?
We can compute this term recursively: we know the relationship between the current state and the last one and can use that to figure out the relationship between the current one and the prior.

## Slide 81: Let’s start with filtering Where is the robot now?
We can compute this term recursively: we know the relationship between the current state and the last one and can use that to figure out the relationship between the current one and the prior.

## Slide 82: Let’s start with filtering Where is the robot now?
We can compute this term recursively: we know the relationship between the current state and the last one and can use that to figure out the relationship between the current one and the prior.
Also, a probability distribution over the states is known as the “belief” or “belief distribution”. Often notated as bt or Bel(t) or just P(x).

## Slide 83: Let’s start with filtering Where is the robot now?
We can use what we know about probability to write this in terms of distributions and terms we know:

## Slide 84: Let’s start with filtering Where is the robot now?
Our filtering equation looks as follows:
It’s often easiest to represent this as a two-stage problem.
Prediction Step:
From robot motion
Update Step:
From observation

## Slide 85: What if I see Yellow at time t=1?
First, we go for the prediction step:

## Slide 86: What if I see Yellow at time t=1?
First, we go for the prediction step:

## Slide 87: What if I see Yellow at time t=1?
Next we need to run the “update” step, which corresponds to receiving an observation:
What elements do we take from the matrix?

## Slide 88: What if I see Yellow at time t=1?
Next we need to run the “update” step, which corresponds to receiving an observation:

## Slide 89: Putting both steps together

## Slide 90: What if we predict again?
We see something that looks like the following:
Why does our “confidence” decrease?
What is the physical origin of this?

## Slide 91: Temporal Inference has multiple tasks we could want to solve

## Slide 92: Temporal Inference has multiple tasks we could want to solve

## Slide 93: How do we “predict”?

## Slide 94: How do we “predict”?
We’ve already done it!
We run the “predict” operation but don’t “update” (since we haven’t received another observation)

## Slide 95: Temporal Inference has multiple tasks we could want to solve

## Slide 96: Next is smoothing
Using more recent measurements, we can get a better understanding of where we used to be.
Think of GPS: if I was just wandering around for a while and we get a GPS measurement, I can better estimate both where I am now and also where I was for the last few time steps.

## Slide 97: Next is smoothing
Using more recent measurements, we can get a better understanding of where we used to be.
Think of GPS: if I was just wandering around for a while and we get a GPS measurement, I can better estimate both where I am now and also where I was for the last few time steps.

## Slide 98: The forward message is just filtering, but we also need a “backwards message”
Filtering involves passing information forwards in time.
“Backwards filtering” passes information from later time steps

## Slide 99: Temporal Inference has multiple tasks we could want to solve

## Slide 100: The “best sequence” problem
Imagine that I want to know how far I’ve traveled from my noisy measurements: to compute an accurate total distance, we need to know where we’ve been at each time.
Application: using GPS while running.
We’ve basically already solved this problem: