## Slide 1: CS 485 Autonomous Robotics Localization II
Prof. Xuesu Xiao
George Mason University
Slides Credits: Gregory Stein

## Slide 2: Logistics
Homework 3 due April 7 before class
Mid-project presentation April 14
  Check out your laptop projection before class

## Slide 3: Reminder… Prediction and Update
The Kalman Filter: continuous (gaussian) filtering

## Slide 4: Motion Model
Sources of motion error:

## Slide 5: Sensor Model

## Slide 6: Motion so far comes from odometry, but what if we don’t have it?
Rather than comparing laser scans against a known map, we can compare them to one another: “scan matching”

## Slide 7: Scan Matching: comparing consecutive scans to figure out how far we’ve moved

## Slide 8: Scan Matching: comparing consecutive scans to figure out how far we’ve moved

## Slide 9: Scan Matching via “Iterative Closest Point”

## Slide 10: Iterative Closest Point

## Slide 11: Iterative Closest Point
Issues? It’s a bit sensitive to outliers.
What if there are points in one set that don’t exist in the other?
This happens often in practice: noise, reflections, motion between the scans. We need an approach that is robust to outliers.

## Slide 12: But First… Linear Algebra A Crash Course

## Slide 13: Least Squares Solving

## Slide 14: Least Squares is used to solve, for example, curve fitting problems
Linear regression:

## Slide 15: Least Squares is used to solve, for example, curve fitting problems
Linear regression:

## Slide 16: So how do we solve this problem?
Let’s look at this from a net cost perspective. I have N points:
The residuals specify the “error”:
We want the beta’s that minimize
this error.

## Slide 17: We want to minimize the Sum of Squared Error (or Mean Squared Error)

## Slide 18: We want to minimize the Sum of Squared Error (or Mean Squared Error)
So how do we solve for this?

## Slide 19: If we write this as a matrix equation, we can solve it using linear algebra.
From CMU Statistics Course

## Slide 20: If we write this as a matrix equation, we can solve it using linear algebra.
From CMU Statistics Course

## Slide 21: If we write this as a matrix equation, we can solve it using linear algebra.
From CMU Statistics Course

## Slide 22: If we write this as a matrix equation, we can solve it using linear algebra.
From CMU Statistics Course

## Slide 23: If we write this as a matrix equation, we can solve it using linear algebra.
From CMU Statistics Course

## Slide 24: If we write this as a matrix equation, we can solve it using linear algebra.
From CMU Statistics Course

## Slide 25: Many problems in robot state estimation are least-squares problems

## Slide 26: Many problems in robot state estimation are least-squares problems
Also, this is the “Pseudo-inverse” of x:
It allows us to “invert” a matrix that isn’t square.
Note that if the matrix is square, this will allows us to solve for a line that exactly fits the parameters. No pseudo-inverse required.

## Slide 27: Eigenvalues and Eigenvectors

## Slide 28: What are eigenvalues and eigenvectors?
Source: Wikipedia

## Slide 29: We can also rewrite a matrix using its eigenvalues and eigenvectors
Source: Wikipedia

## Slide 30: We can also rewrite a matrix using its eigenvalues and eigenvectors
Source: Wikipedia

## Slide 31: Matrix Factorization

## Slide 32: There are many different ways of “factorizing” matrices
Source: Wikipedia

## Slide 33
Singular Value Decomposition is similar but for non-square matrices

## Slide 34: RANSAC
Handling outliers in data

## Slide 35: Reading & Slide Credits
Slide Credits (from which many of these slides are either directly taken or adapted)
Cornell Tech Computer Vision Course (Noah Snavely)
CMU Computer Vision Course
Penn State Computer Vision Course
Stanford: Stats 203

## Slide 36: So how do we make what is obvious to us visible to the computer (via an algorithm)?

## Slide 37: Outliers are (roughly) points that don’t agree with our model of the problem
Let’s fit a line to some data:

## Slide 38: Outliers are (roughly) points that don’t agree with our model of the problem
Let’s fit a line to some data:
This is the line I want…

## Slide 39: Outliers are (roughly) points that don’t agree with our model of the problem
Let’s fit a line to some data:
This is the line I want, but the residuals for those two outlying points are enormous.

## Slide 40: Outliers are (roughly) points that don’t agree with our model of the problem
Let’s fit a line to some data:
The actual line I fit to all the data (roughly) looks like this, because it minimizes the sum of squared residuals.

## Slide 41: Outliers are (roughly) points that don’t agree with our model of the problem
Let’s fit a line to some data:
If we split these points into inliers and outliers (somehow), we could fit the line we wanted to the inlying data and ignore the outliers.

## Slide 42: Outliers are (roughly) points that don’t agree with our model of the problem
Let’s fit a line to some data:
If we split these points into inliers and outliers (somehow), we could fit the line we wanted to the inlying data and ignore the outliers.
Inliers
Outlier
Outlier

## Slide 43: Outliers are (roughly) points that don’t agree with our model of the problem
Let’s fit a line to some data:
If we split these points into inliers and outliers (somehow), we could fit the line we wanted to the inlying data and ignore the outliers.
Inliers
Outlier
Outlier

## Slide 44: Robust Estimation via Random Sample Consensus
RANdom Sample Consensus (a.k.a RANSAC) is a very common and relatively simple procedure for detecting outliers.
The general procedure involves two steps (performed repeatedly):
Split the data into inliers and outliers
Fit the model parameters to the inliers (ignoring outliers)
Original Paper: M. A. Fischler and R. C. Bolles (June 1981). "Random Sample Consensus: A Paradigm for Model Fitting with Applications to Image Analysis and Automated Cartography". Comm. of the ACM 24: 381—395.

## Slide 45: Robust Estimation via Random Sample Consensus
In RANSAC: We pick a random set of points (”s” of them) to be inliers, and fit our model to those, and count the number of inliers: points that are below some distance/residual threshold.
We repeatedly conduct this procedure and pick the model parameters that maximize the number of inliers.
Why can’t we just pick the one with the lowest sum of squared residuals for the inlying points?

## Slide 46: Robust Estimation via Random Sample Consensus
In RANSAC: We pick a random set of points (”s” of them) to be inliers, and fit our model to those, and count the number of inliers: points that are below some distance/residual threshold.

## Slide 47: Robust Estimation via Random Sample Consensus
Fit to 2 yellow points
In RANSAC: We pick a random set of points (”s” of them) to be inliers, and fit our model to those, and count the number of inliers: points that are below some distance/residual threshold.

## Slide 48: Robust Estimation via Random Sample Consensus
Fit to 2 yellow points
Inliers: 4
In RANSAC: We pick a random set of points (”s” of them) to be inliers, and fit our model to those, and count the number of inliers: points that are below some distance/residual threshold.

## Slide 49: Robust Estimation via Random Sample Consensus
Fit to 2 yellow points
In RANSAC: We pick a random set of points (”s” of them) to be inliers, and fit our model to those, and count the number of inliers: points that are below some distance/residual threshold.

## Slide 50: Robust Estimation via Random Sample Consensus
Fit to 2 yellow points
Inliers: 6
In RANSAC: We pick a random set of points (”s” of them) to be inliers, and fit our model to those, and count the number of inliers: points that are below some distance/residual threshold.

## Slide 51: Robust Estimation via Random Sample Consensus
Fit to 2 yellow points
In RANSAC: We pick a random set of points (”s” of them) to be inliers, and fit our model to those, and count the number of inliers: points that are below some distance/residual threshold.

## Slide 52: Robust Estimation via Random Sample Consensus
Fit to 2 yellow points
Inliers: 19
In RANSAC: We pick a random set of points (”s” of them) to be inliers, and fit our model to those, and count the number of inliers: points that are below some distance/residual threshold.

## Slide 53: Robust Estimation via Random Sample Consensus
Fit to 2 yellow points
In RANSAC: We pick a random set of points (”s” of them) to be inliers, and fit our model to those, and count the number of inliers: points that are below some distance/residual threshold.

## Slide 54: Robust Estimation via Random Sample Consensus
Fit to 2 yellow points
Inliers: 13
In RANSAC: We pick a random set of points (”s” of them) to be inliers, and fit our model to those, and count the number of inliers: points that are below some distance/residual threshold.

## Slide 55: Robust Estimation via Random Sample Consensus
We pick the line that has the most inliers.
In RANSAC: We pick a random set of points (”s” of them) to be inliers, and fit our model to those, and count the number of inliers: points that are below some distance/residual threshold.

## Slide 56: Robust Estimation via Random Sample Consensus
We pick the line that has the most inliers.
In practice, we usually re-fit the line to all the inliers once the best line is chosen.
In RANSAC: We pick a random set of points (”s” of them) to be inliers, and fit our model to those, and count the number of inliers: points that are below some distance/residual threshold.

## Slide 57: Robust Estimation via Random Sample Consensus
Why can’t we just pick the one with the lowest sum of squared residuals for the inlying points?

## Slide 58: Robust Estimation via Random Sample Consensus
Why can’t we just pick the one with the lowest sum of squared residuals for the inlying points?

## Slide 59: Robust Estimation via Random Sample Consensus
Why can’t we just pick the one with the lowest sum of squared residuals for the inlying points?
The residual of this line (which has only 2 inliers) is zero…

## Slide 60: Lots of questions remain!
How do we decide what it means to be an inlier?
How many samples do we need to ensure good performance?
What does it even mean to have good performance?

## Slide 61: We often assume that the noise follows some sort of Gaussian distribution
In order to decide what an inlier or an outlier looks like, we need to choose a noise model: usually, it’s Gaussian, with some standard deviation (e.g. 3 pixels).

## Slide 62: We often assume that the noise follows some sort of Gaussian distribution
In order to decide what an inlier or an outlier looks like, we need to choose a noise model: usually, it’s Gaussian, with some standard deviation (e.g. 3 pixels).

## Slide 63: We can select inliers by thresholding via a Chi-Squared test
For a 1-dimensional system, like fitting a line, a threshold of
yields 95% inliers.
(5.99 for 2D)

## Slide 64: How many times (“rounds” N) should we run the system?
If we need to choose s samples per round, and we have an outlier ratio e, and we want to get the “right answer” with probability p:
Where did this come from?

## Slide 65: How many times (“rounds” N) should we run the system?
If we need to choose s samples per round, and we have an outlier ratio e, and we want to get the “right answer” with probability p:
The probability a single point is an inlier

## Slide 66: How many times (“rounds” N) should we run the system?
If we need to choose s samples per round, and we have an outlier ratio e, and we want to get the “right answer” with probability p:
The probability that choosing s points yields only inliers

## Slide 67: How many times (“rounds” N) should we run the system?
If we need to choose s samples per round, and we have an outlier ratio e, and we want to get the “right answer” with probability p:
The probability that at least one point was an outlier in one round

## Slide 68: How many times (“rounds” N) should we run the system?
If we need to choose s samples per round, and we have an outlier ratio e, and we want to get the “right answer” with probability p:
The probability that all N rounds have at least one outlier

## Slide 69: How many times (“rounds” N) should we run the system?
If we need to choose s samples per round, and we have an outlier ratio e, and we want to get the “right answer” with probability p:
The probability that after N rounds, we managed to find at least one round of s points that were all inliers.

## Slide 70: How many times (“rounds” N) should we run the system?
If we need to choose s samples per round, and we have an outlier ratio e, and we want to get the “right answer” with probability p:
Solve for N to get the above formula.

## Slide 71: How many times (“rounds”) should we run the system?
If we need to choose s samples per round, and we have an outlier ratio e, and we want to get the “right answer” with probability p:
Solve for N to get the above formula.
This means we need a pretty good idea of the inlier ratio, which means approximating the noise.

## Slide 72: How many times (“rounds”) should we run the system?
If we need to choose s samples per round, and we have an outlier ratio e, and we want to get the “right answer” with probability p:

## Slide 73: How do we pick s (the number of samples per round)?
This is really a matter of the type of problem we’re trying to solve:

## Slide 74: RANSAC: Pros and Cons
Pros (the good):
Simple and general
Can (and and usually is) applicable to many different types of problem
Often works quite well in practice
Cons (the bad):
There are still some parameters to tune, like the inlier ratio or those of the error model
Sometimes it requires too many iterations
Can fail when there are too many outliers

## Slide 75: This is the backbone of many applications like SLAM
https://arxiv.org/pdf/1909.08605.pdf

## Slide 76: This is the backbone of many applications like SLAM
https://arxiv.org/pdf/1909.08605.pdf

## Slide 77: Landmarks

## Slide 78: Let’s revisit the idea of probability distributions being represented as graphs
The graph is a convenient visual tool, but an incredibly powerful way to think about these problems more generally:
What if I removed an observation?
What if I added additional observations and sensors?

## Slide 79: Let’s revisit the idea of probability distributions being represented as graphs
The graph is a convenient visual tool, but an incredibly powerful way to think about these problems more generally:
What if I removed an observation?
What if I added additional observations and sensors?
The probability distribution starts to get quite complicated, but the graph helps us manage that complexity.

## Slide 80: Instead of GPS, the robot may instead need to figure out where it is from landmarks
The robot will detect “stuff” in the environment.
If we see the same thing from different viewpoints, we can triangulate its location and use that to constrain our movement.
Even when our measurements of the landmarks are noisy, each gives us more information about where we are likely to be.

## Slide 81: Modern SLAM: everything is a graph
SLAM: Simultaneous Localization and Mapping
Square Root SAM paper

## Slide 82: Modern SLAM: everything is a graph
Square Root SAM paper

## Slide 83: Modern SLAM: everything is a graph
Square Root SAM paper

## Slide 84: What’s a landmark?
Points of interest
Objects
AR Tags
Other ideas?
From the National Park Service

## Slide 85: Sparse Features: distinguishable points detected and matched between images
From the OpenCV Feature Matching Tutorial

## Slide 86: Landmarks don’t exactly solve all our problems
What if our landmarks move?
How will our graph need to change?

## Slide 87: Landmarks don’t exactly solve all our problems
What if our landmarks move?
How will our graph need to change?
What if we have multiple of the same object (e.g., multiple of the same textbook)
How can we tell which one we’re looking at?

## Slide 88: Landmarks don’t exactly solve all our problems
What if our landmarks move?
How will our graph need to change?
What if we have multiple of the same object (e.g., multiple of the same textbook)
How can we tell which one we’re looking at?
We’ll talk about tracking and data association.