## Slide 1: CS 485 Autonomous Robotics A Gentle Introduction to ROS
Prof. Xuesu Xiao
George Mason University
Slides Credits: Gregory Stein

## Slide 2: Agenda for today
Introduction to ROS
Classmates' introduction for team formation
  Team formation due Feb 5
  Send an email of your team info to the instructor and TA

## Slide 3: Let’s look at some robots
Robots are good for lots of things!
Their application determines their function.

## Slide 4: Clearpath’s Turtlebot

## Slide 5: FRANKA makes some nice robot arms

## Slide 6: A mobile manipulator can both move around and interact with objects
The GMU Autonomous Robotics Lab has a few LoCoBots

## Slide 7: The Baxter and PR2 are both defunct, but the Fetch is solid (and costs ~$100k)

## Slide 8: Boston Dynamic’s Spot is also fantastic

## Slide 9: There are also many available simulation tools: MuJoCo

## Slide 10: There are also many available simulation tools: Bullet Physics

## Slide 11: There are also many available simulation tools: Gazebo

## Slide 12: There are also many available simulation tools: Isaac Sim (from Nvidia)

## Slide 13: Robots in the RobotiXX Lab

## Slide 14: Then, let’s look at some humans
Humans that have been, or will be, building autonomous robots.
Robots will only be as good as the humans that build them (or at least for now when we don’t have Skynet yet…).

## Slide 15: Motivation: We need a system that humans can use to empower the usage of all these robots and tools

## Slide 16: Motivation: We need a system that empowers us to use all these robots
From: Sutton & Barto, Reinforcement Learning

## Slide 17: Motivation: We want to break up robot capabilities into composable blocks

## Slide 18: Motivation: We want to break up robot capabilities into composable blocks
From: https://www.researchgate.net/figure/Flowchart-of-Stanley-software-system-The-software-is-roughly-divided-into-six-main_fig17_224773193

## Slide 19: Introduction to ROS
The Robot Operating System is used on many robots.

## Slide 20: ROS: The Robot Operating System
So what’s ROS?
Is it really an “operating system”? Well it’s not a file system, but it does (true to its name) operate robots.
ROS is more of an orchestration system: it’s what spawns different processes and handles communication between them and sensors and motors, etc.

## Slide 21: Robots often need many of the same capabilities
Earlier, we discussed many different types of robots. There are overlapping capabilities between them. They may use the same sensors, the same algorithms, etc…
We could make a monolithic system, but it would be somewhat difficult to design such systems.

## Slide 22: Robot systems tend to be modular
ROS is going to be our way of managing, building, running these processes.

## Slide 23: ROS Master (roscore): The process you run to connect the pieces (“nodes”)
Command: roscore

## Slide 24: Here’s a simple example of a robot with a camera and an image processing node

## Slide 25: ROS also supports remote access

## Slide 26: Some ROS terminology
Core Concepts:
A “node” is a single ROS process
A “topic” is a named channel on which data can be shared
A “message” is a piece of data shared by a “topic”
Functionality:
A “publisher” is a function that sends data to a topic (often run within Python or C++).
A “subscriber” is a function that listens for messages on a topic; when a new message appears on a topic, the subscriber’s associated function is run with that message as input.

## Slide 27: Commands to publish and listen to a topic
roscore # Start ros
rostopic list # Look at the topics
rostopic pub /hello std_msgs/String "Hello Robot"
rostopic list # Look at the topics again (/hello is there)
rostopic echo /hello # Listen to that topic
rosnode list
rosnode info
rostopic info /hello

## Slide 28: roslaunch Launch files use XML syntax to spin up multiple processes at once

## Slide 29: roslaunch Launch files use XML syntax to spin up multiple processes at once

## Slide 30: Launch files are incredibly useful
With a single file, we can spin up a suite of sensors and processes, algorithms, etc.

## Slide 31: RVIZ: the ROS visualizer

## Slide 32: Gazebo is a simulator that is meant to integrate with ROS

## Slide 33: Publishing to a topic that drives a robot

## Slide 34: ROS has many tools for visualization, logging, and inspection

## Slide 35: ROS has many tools for visualization, logging, and inspection
A similar command is
rosrun rqt_tf_tree rqt_tf_tree

## Slide 36: A ROS Publisher
From the ROS Tutorials

## Slide 37: A ROS Listener
From the ROS Tutorials

## Slide 38: ROS also comes with a build system: Catkin
We need to run catkin to let ROS know that these new processes exist.
A “workspace” is a folder that contains code for multiple packages. catkin_make “builds” the code (or in the Python case, let’s ROS know that these nodes exist).

## Slide 39: rosrun spawns a single node from a single package (like a single line from a launch file)

## Slide 40: rosrun spawns a single node from a single package (like a single line from a launch file)

## Slide 41: Let’s do some inspecting
rostopic list # Look at the topics again (/hello is there)
rostopic echo /hello # Listen to that topic
rosnode list
rosnode info
rostopic info […]

## Slide 42: ROS also supports recording and playing back data
The “rosbag” tool is quite useful. It records messages on a set of specified topics and can play it back in a number of ways.
We can play back the data in real time
We can play back the data faster or more slowly
We can step through the datum one at a time (to avoid any issues of timing or dropping messages) in Python or C++

## Slide 43: ROS has many different “message types” and “composite messages”

## Slide 44: Classmates introduction for team formation
Introduce yourself to the whole class in 1 min
  Who are you? Which year are you in? Which major are you in?
  Why are you interested in robotics?
  What is your skillset? Math? Hardware? System? Programming? C++? Python?
  What kinds of robotics project would you like to work on?