## Slide 1: CS 685 Autonomous Robotics Localization I
Prof. Xuesu Xiao
George Mason University
Slides Credits: Gregory Stein

## Slide 2: Logistics Notes
Good job on the BARN Challenge submissions!
While your navigation system will be evaluated during spring break, please prepare a 5-min presentation about the approach you took to tackle the BARN Challenge during class on March 22.
We will discuss our approaches with the evaluation scores as a reference. 

## Slide 3: Last week, just about everything was Gaussian: Motion Model
How do we compute the “uncertainty” on each?

## Slide 4: Last week, just about everything was Gaussian: Sensor Model
How do we compute the “uncertainty” on each?
How do we incorporate the GPS observations?

## Slide 5: However, our graphical representation was more general
The graphical representation will look pretty much the same:

## Slide 6: The EKF is necessary when we have a robot with orientation
If we have uncertainty in yaw, the motion model becomes nonlinear:
From: https://cs.gmu.edu/%7Ekosecka/cs685/cs685-11-sensor-motion-models.pdf

## Slide 7: The EKF is necessary when we have a robot with orientation
If we have uncertainty in yaw, the motion model becomes nonlinear:
From: https://cs.gmu.edu/%7Ekosecka/cs685/cs685-11-sensor-motion-models.pdf

## Slide 8: Will the EKF help us with the “Doors” example from earlier?

## Slide 9: Will the EKF help us with the “Doors” example from earlier?
Hmm, probably not. We approximate the distribution as being Gaussian, so we’d lose the multi-peaked structure.
We’ll talk more about how to handle more complex probability distributions like these.

## Slide 10: Motion and Sensor Models

## Slide 11: Robot motion is inherently uncertain
Last week, we talked about both Gaussian Motion and Observations, but in general, neither will be. We need ways to represent non-Gaussian models.

## Slide 12: Reminder: graphical representations of joint probability distributions

## Slide 13: Consider a differential drive robot: Wheel encoders tell us the rotation

## Slide 14: Dead Reckoning: integrating motion measurements to compute position
Mathematical procedure for determining the present location of a vehicle.
Achieved by calculating the current pose of the vehicle based on its velocities and the time elapsed.
Last week, we talked about this in the context of Gaussian Motion and the noisy motion estimates:

## Slide 15: Even if we could perfectly integrate the wheel encoders, our measurements are noisy
Sources of motion error:

## Slide 16: Odometry Model

## Slide 17: A noise model for odometry for a differential drive robot

## Slide 18: A noise model for odometry for a differential drive robot

## Slide 19: Calculating the posterior from our (noisy) motion model:
P(x’ | x, u)

## Slide 20: We repeatedly apply this motion model to get the posterior on the position

## Slide 21: How do we use this motion model?
A Kalman Filter requires that everything be Gaussian.
The Extended Kalman Filter approximates the nonlinear system as being Gaussian, which works fairly well for a while, but over time—especially when dead reckoning, and there are no updates from other measurements—you start to lose accuracy.
What if we tried sampling again?

## Slide 22: Reminder: Let’s say you wanted to compute the area of a circle…
What if you printed out the shape and threw a dart at it?
If you aim is totally random, what’s the probability you’re inside the square, but not the circle?
Image Credit
P = 1 - Acircle / Asquare

## Slide 23: Reminder: Monte Carlo Sampling
Idea: we throw a lot of darts and the number that are inside the circle will tell us what it’s area is.
As we get more samples, our approximation gets better.
In many cases, this can be way faster than trying to get an exact solution.
Image: Wikipedia

## Slide 24: Now, we have a probability distribution that we cannot easily write down…
We can sample values from the distribution and we’ll represent that distribution with points drawn from that distribution.
Idea: we have some random value x ~ P(X). If we can draw many values of x, we can use those as a stand in for the distribution. With enough samples, we can compute any value we would want that requires the distribution:

## Slide 25: Sample-based Density Representation

## Slide 26: Sampled Normal Distribution

## Slide 27: Sampled Triangular Distribution

## Slide 28: We can use this to sample from our noisy motion model

## Slide 29: We can use this to sample from our noisy motion model

## Slide 30: We can use this to sample from our noisy motion model

## Slide 31: Another Example: a velocity-based model

## Slide 32: Another Example: a velocity-based model

## Slide 33: Another Example: a velocity-based model

## Slide 34: Another Example: a velocity-based model

## Slide 35: Overview: Non-Gaussian Motion Models

## Slide 36: Sensor Models
How do we measure the world around us?

## Slide 37: There are many ways robots sense the world

## Slide 38: LiDAR: Light Detection and Ranging
Video from the MIT Team

## Slide 39: Velodyne makes great LiDARs
The Puck
Link: https://velodynelidar.com/products/puck/

## Slide 40: Proximity Sensors: lasers and sonars

## Slide 41: Beam-based (probabilistic) sensor model

## Slide 42: Beam-based (probabilistic) sensor model

## Slide 43: Typical types of errors for beam-like measurements

## Slide 44: Proximity measurements and sources of noise and error

## Slide 45: Beam-based proximity model

## Slide 46: Beam-based proximity model

## Slide 47: Beam-based proximity model

## Slide 48: We can collect data for ranges of an object a known distance away

## Slide 49: We can determine the model parameters by fitting to the data

## Slide 50: Here are how the model compares to the data:

## Slide 51: Here are some examples of laser scans in a physical environment

## Slide 52: Summary of a beam-based sensor measurement model

## Slide 53: What about a “scan-based” measurement model?

## Slide 54: What about a “scan-based” measurement model?

## Slide 55: What about a “scan-based” measurement model?

## Slide 56: What about a “scan-based” measurement model?

## Slide 57: What about a “scan-based” measurement model?

## Slide 58: We can use probabilistic sensor models to perform multiple operations we may need:

## Slide 59: Will the EKF help us with the “Doors” example from earlier?

## Slide 60: Will the EKF help us with the “Doors” example from earlier?
Hmm, probably not. We approximate the distribution as being Gaussian, so we’d lose the multi-peaked structure.
Now, we’ll talk more about how to handle more complex probability distributions like these.

## Slide 61: What if we discretize the space?
The Belief can be split into ”buckets” each with some “weight”
Motion “moves” the probability mass around
Measurements update the belief.
[Same as before, but no longer continuous.]

## Slide 62: What if we discretize the space?
The Belief can be split into ”buckets” each with some “weight”
Motion “moves” the probability mass around
Measurements update the belief.
[Same as before, but no longer continuous.]

## Slide 63: The Discrete Bayes Filter Implementation

## Slide 64: Example application: grid-based localization Figure out where we are from scans

## Slide 65: Sample-based localization
We get sensor observations and we know how much we move between observations

## Slide 66: By getting sensor measurements and connecting them with motion, we can figure out the pose:

## Slide 67: Introducing the “Particle Filter”

## Slide 68: Particle filter: mathematical formalism

## Slide 69: Function approximation using particles

## Slide 70: Rejection Sampling

## Slide 71: We don’t often want to sample everywhere, so we can use “Importance Sampling”

## Slide 72: Particle Filtering Start with a uniform distribution of particles

## Slide 73: Particle Filtering We next compute weights from an observation

## Slide 74: Particle Filtering We move/update particles using the motion model and resample

## Slide 75: Particle Filtering We next compute weights from an observation

## Slide 76: Particle Filtering We move/update particles using the motion model and resample

## Slide 77: Particle Filter Algorithm

## Slide 78: Particle Filter Algorithm

## Slide 79: Particle Filter Algorithm

## Slide 80: How does resampling work?

## Slide 81: Mobile Robot Localization

## Slide 82: Mobile Robot Localization
Non-Gaussian Motion Model
Very non-Gaussian sensor model

## Slide 83: Particle Filtering Example Start with a uniform particle distribution

## Slide 84: Particle Filtering Example Get an observation

## Slide 85: Particle Filtering Example Move and resample

## Slide 86: Particle Filtering Example Get an observation

## Slide 87: Particle Filtering Example Move and resample

## Slide 88: Particle Filtering Example Get an observation

## Slide 89: Particle Filtering Example Move and resample

## Slide 90: We can do the same thing but with vision Vision-based localization

## Slide 91: Vision-based localization Observation: Under a light

## Slide 92: Vision-based localization Observation: Next to a light

## Slide 93: Vision-based localization Observation: not near a light

## Slide 94: Vision-based localization Combined we can figure out where we are

## Slide 95: Limitations of particle filtering

## Slide 96: Approaches to deal with limitations

## Slide 97: Particle Filters

## Slide 98: Particle Filter Localization